## Slide 1: LCC Fusion Hardware Architecture Overview
Open-Source, Tiered, Expandable, Designed for Learning
Pat Fleming
Email: PatFlemingHTC@Gmail.com
Notes: (voice: Nelson) Before we start… this is really the big picture, right? What Fusion is, why it exists, and how all the pieces fit together?
(pause: 0.8)
(voice: Harrison) Exactly. This whole session explains the architecture behind Fusion — why it’s open-source, how it scales, and how the cards and busses all work together.
(pause: 1.0)

## Slide 2: Why Fusion Exists
Open Source & Education
Fusion is 100% open-source
All schematics, PCB files, and firmware are public
Built for education and DIY electronics
Encourages STEM-style learning
For hobbyists who want to understand electronics
Community-driven, not commercial
Notes: (voice: Nelson) Before we talk hardware… why make Fusion open-source?
(pause: 0.8)
(voice: Harrison) Because it’s built for learning. People can read the designs, modify them, and build their own cards.
(pause: 0.8)
(voice: Nelson) So it’s a STEM-style project for model railroaders?
(pause: 0.8)
(voice: Harrison) Exactly. Fusion teaches real electronics — while running trains.
(pause: 1.0)

## Slide 3: Fusion Hardware Architecture
3-Tier Overview
Fusion uses a 3-tier distributed design
Each tier has one job
System scales cleanly
Add new hardware without redesign
Architecture stays stable
Notes: (voice: Nelson) Three tiers? Why not just one big board?
(pause: 0.8)
(voice: Harrison) Because each tier does one job well. That’s what keeps Fusion simple and expandable.
(pause: 1.0)
(voice: Nelson)
Got it
so let’s look at each tier next.
(pause: 1.0)

## Slide 4: Tier 1: The Node Card
Tier 1 = the brain
Runs logic and CAN
Defines the node’s purpose
Fusion has three Node boards
Different processors, same role
Notes: (voice: Nelson) So Tier 1 is always the Node card?
(pause: 0.8)
(voice: Harrison) Right. It’s the processor, and each node runs its own logic independently.
(pause: 0.8)
(voice: Nelson) And Fusion already supports different processors?
(pause: 0.8)
(voice: Harrison) Yes — all ESP32-based, but currently three very different options.
(pause: 0.6)
(voice: Harrison) We use the ESP32-S3 SuperMini on the Quad-Node Card. It actually gives you four independent LCC Nodes on one inexpensive card. That means you can split responsibilities — one Node for inputs, one for signals, one for sounds, one for specialty tasks — all in a very small footprint.
(pause: 1.0)
(voice: Harrison) Then there’s the Node Card with a single ESP32-S2. That’s our most common processor — full capabilities, good memory, and a few more I/O lines.
(pause: 0.8)
(voice: Harrison) And the newest is the P4-Node Card, built on the ESP32-P4. It has much more memory, perfect for more complex configuration and logic sets, but to make sue of Wi-Fi or Bluetooth, you would need to add one of the other types of Node Cards to your cluster.
(pause: 1.0)

## Slide 5: Tier 2: I/O Cards
Tier 2 = cards that do the work
Turnout, Signal, Detection, Sensor, Audio, PWM…
Over 10 I/O cards exist
Each card does one job
Combine them to create node types
Notes: (voice: Nelson) Now for tier 2. So, this must be the “action layer,” right?
(pause: 0.8)
(voice: Harrison) Exactly. Each card controls a function — turnout, audio, sensors, lighting.
(pause: 0.8)
(voice: Nelson) And any combo is allowed?
(pause: 0.8)
(voice: Harrison) Yes. Mix and match to build whatever node you need.
(pause: 1.0)

## Slide 6: TIER 3: Breakout Boards + Devices
Breakout boards adapt cards to physical devices
Connect using network cables
Devices connect via screw terminals, JST, servo cables
Example: Turnout Card → 4 different breakouts
Supports many switch machine types
Notes: (voice: Nelson) So Tier 3 is where the wires hit real hardware?
(pause: 0.8)
(voice: Harrison) Exactly. Breakouts adapt the signals into motors, LEDs, servos — all the physical devices.
(pause: 0.8)
(voice: Nelson)
I think I need an example. Is useful for Turnout Card that must support different types of switch machines?
(pause: 0.8)
(voice: Harrison) Yes. The Turnout Card is a perfect example of this. Just pick the breakout board you need for the type of switch machine used on the turnout.
Fusion already has breakout boards for several common switch machines — stall motor, slow motion, servo motors, and coils.
Simply cable the correct breakout board to the Turnout Card and you’re all set.
Different breakout boards are supported by the same Turnout Card.
Additional switch machines can be supported by creating more breakout boards.
(pause: 1.0)

## Slide 7: Fusion Busses Three Busses, Three Jobs
Fusion uses three buses, each with a single purpose
CAN Bus: connects nodes across the layout
Node Bus: connects the Node to all cards in its cluster
COMM Bus (I²C): connects the Node to I/O cards & peripherals
One bus per job = clean, simple design
Notes: (voice: Nelson)
So… Fusion doesn’t just have one bus?
(pause: 0.8)
(voice: Harrison)
No — and that’s a good thing.
Each bus has one job, which keeps everything clean.
(pause: 0.8)
(voice: Nelson)
Okay, walk me through it?
(pause: 0.8)
(voice: Harrison)
The kanBus links nodes across the whole layout.
The Node Bus carries power and communications from the Node Card to the other cards in its cluster.
And the COMM Bus, which uses I2C serial communications, lets the Node Card talk directly to the Fusion I/O cards and LCD displays.
(pause: 0.8)
(voice: Nelson)
So one for the layout, and two inside the Node Cluster for connections and communications?
(pause: 0.8)
(voice: Harrison)
Exactly.
Three busses. Three jobs. Nice and simple.
(pause: 1.0)

## Slide 8: Design Architecture Modeled After Desktop Computers
Standard card form factor
Inspired by ATX motherboards / PCI cards
Node plugs into a backplane
Cards connect the same way every time
Breakouts adapt to devices
Notes: (voice: Nelson)
So… why make all the Fusion cards the same size and shape?
What does that actually help with?
(pause: 0.8)
(voice: Harrison)
Because this is the same approach desktop computers have used for over 30 years.
Standard form factors — like ATX motherboards, connectors, and PCIe — keep everything compatible and easy to upgrade.
(pause: 0.8)
(voice: Nelson)
Compatible… how?
(pause: 0.8)
(voice: Harrison)
When every card shares the same physical layout and the same edge connector,
the system always knows where power, CAN, and I2C will be.
That means any card can plug into any Hub slot without rewiring or redesigning anything.
(pause: 0.8)
(voice: Nelson)
So the cards stay standardized no matter what new features you add?
(pause: 0.8)
(voice: Harrison)
Exactly.
The cards stay consistent and predictable — just like PC expansion cards.
That’s what lets Fusion grow without breaking the architecture.
Cards are designed to fit into the Node Bus Hub for power and communications. Have consistent mounting holes and
Connectors to the breakout boards.
(pause: 0.8)
(voice: Nelson)
Okay… but what about all the different devices people connect?
Motors, LEDs, coils, servos… that’s a lot of wiring.
(pause: 0.8)
(voice: Harrison)
That’s where the breakout boards come in.
They handle the real-world wiring. Standardized to 50mm to fit into the UM 50 Profile PCB housing and holes for mounting.
Network cable connect back to the parent card.
The I/O card sends the signals,
and the breakout adapts those signals to the physical connectors the device actually needs.
(pause: 0.8)
(voice: Nelson)
So the cards stay the same, and the breakouts handle all the variations?
(pause: 0.8)
(voice: Harrison)
Exactly.
Cards stay consistent.
Breakouts stay flexible.
It keeps Fusion clean, expandable, and easy to work with.
(pause: 1.0)

## Slide 9: Why Tiers Matter
Add new Node boards without redesign
Add new I/O cards instantly
Add new breakouts for new devices
System grows without rewiring
Architecture stays stable
Notes: (voice: Nelson)
So the tiers make Fusion grow cleanly?
(pause: 0.8)
(voice: Harrison)
Exactly.
The whole point of having three tiers is to keep everything organized.
Each tier has one job, and that makes the system easy to expand.
(pause: 0.8)
(voice: Nelson)
But how does that actually help when you're adding new hardware?
(pause: 0.8)
(voice: Harrison)
Well, the Node Card in Tier 1 handles all the logic and communications over the kanbus.
That stays the same.
Tier 2 is just the I/O cards — turnout, signal, detection, audio, sensors.
You can add a brand-new I/O card, and the architecture doesn’t change at all.
(pause: 0.8)
(voice: Nelson)
So the Node doesn’t care what the I/O card does?
It just talks to it?
(pause: 0.8)
(voice: Harrison)
Right.
As long as the card follows the standard Fusion form factor and uses the I2C COMM Bus,
the Node can talk to it instantly.
No hardware redesign.
(pause: 0.8)
(voice: Nelson)
And Tier 3 — the breakout boards — those change too, right?
(pause: 0.8)
(voice: Harrison)
All the time.
You can design a new breakout board for a new motor or sensor,
and the Tier-2 card doesn’t need to change.
The Node doesn’t need to change.
Only the breakout changes — and that’s the whole point of having the tiers separate.
(pause: 0.8)
(voice: Nelson)
So tiers basically stop everything from getting tangled together?
(pause: 0.8)
(voice: Harrison)
Exactly.
Tiers isolate the responsibilities.
Tier 1 runs logic.
Tier 2 handles functions.
Tier 3 adapts to real-world hardware.
That way, Fusion grows sideways — not upward in complexity.
(pause: 1.0)

## Slide 10: Fusion Ecosystem Work in Progress
Fusion architecture is fully designed, but still evolving
Node Boards, I/O Cards, and Breakout Boards are in active development
Hardware and firmware continuously improving
Documentation and assembly guides being built out
Not GA — early adopters & contributors only
Open-source community shaping the final ecosystem
Notes: (voice: Nelson) So everything we’ve shown… is it all out there and ready for everyone right now?
(pause: 0.8)
(voice: Harrison) Not yet. Fusion is still a work in progress. The architecture is solid, the card designs are real, but we’re still building the final ecosystem.
(pause: 0.8)
(voice: Nelson) So it’s not GA — it’s more like early access?
(pause: 0.8)
(voice: Harrison) Exactly. This is the stage where we’re focused on documentation, along with testing of the hardware and firmware before a wider release.
(pause: 1.0)

## Slide 11: Bringing It All Together
Open-source foundation
Tiered architecture
Standard card form factor
Breakouts for device flexibility
Built for learning, building, and expanding
Notes: (voice: Nelson)
So Fusion is open-source, expandable, and built like a desktop computer?
(pause: 0.8)
(voice: Harrison)
Exactly.
But there’s one more important part.
Fusion fits directly into the existing NMRA LCC ecosystem.
It’s not replacing anything — it’s extending what the LCC open-source project already created.
(pause: 0.8)
(voice: Nelson)
Extending it how?
(pause: 0.8)
(voice: Harrison)
Fusion adds more hardware, more software, and a lot more documentation.
It builds on the standard LCC tools, LCC events, and the open-source libraries people already use.
We’re just adding a complete, well-documented system on top of it.
(pause: 0.8)
(voice: Nelson)
So Fusion is basically another open-source project in the same family?
(pause: 0.8)
(voice: Harrison)
Exactly.
It follows the same LCC rules and standards.
It uses the same kanbus messages and the same event model.
Everything we do fits naturally into the broader LCC environment.
(pause: 0.8)
(voice: Nelson)
And anyone using Fusion can still mix it with other LCC hardware?
(pause: 0.8)
(voice: Harrison)
Absolutely.
That’s the whole idea.
Fusion gives people more choices — more nodes, more cards, more breakout boards, and more documentation — all built on the existing open-source foundation.
(pause: 0.8)
(voice: Nelson)
So Fusion isn’t a new universe.
It’s a big expansion pack for the LCC universe?
(pause: 0.8)
(voice: Harrison)
Exactly.
A modern engineering platform that lives inside the LCC world,
extends it,
and gives hobbyists and developers everything they need to build, learn, and innovate.
(pause: 1.0)